## Slide 1: Speech and Audio CSCI 3002 Fall 2018
Notes: Google Pixel Buds image from mashable.com

## Slide 2: Today
Exploring audio in user interfaces
  Incidental audio output
  Audio only interfaces
  Speech input

## Slide 3: Audio

## Slide 4: Audio experiences
Talk with your neighbor about positive/negative experiences in *audio* in interactive systems (games, software, appliances, other devices)
  and why?

## Slide 5: Good & bad uses of audio

## Slide 6: Good & bad uses of audio
Passive audio status
  Fridge
  Car lights on
White noise (mute conversations)
  but creepy?
“I’m listening” feedback (Google Assistant, Amazon Echo)
Annoying reminder
  Smoke detector battery indicator
  Appliances with harsh sounds
  Unexplained / confusing
Repetitive notifications can be distracting
No feedback about audio routing?

## Slide 7: Audio
How it works
Audio as secondary output (multimodal user interfaces)
Data sonification

## Slide 8: Why discuss audio?
Can improve the experience of traditional / graphical user interfaces
Increasingly important in non-visual user interfaces
Applications to accessibility and universal design
Understanding audio can help in making better UIs, can prepare you for upcoming design trends
Notes: Some would even consider this not part of the UI…

## Slide 9: Benefits of audio
Can be used when visual attention is elsewhere
Additional bandwidth — audio processing (generally) does not interfere with visual processing
Can fade into background, grab attention when needed
  Certain sounds can attract attention (“cocktail party effect”)
Speech can be input at a distance
Applications to accessibility, wearable technology, Internet of things stuff

## Slide 10: Drawbacks of audio
Recognition of specific sounds can be very difficult
Limited bandwidth (vs. visual channel)
  Simultaneous audio is challenging
  Longer messages take more time to transmit
Transient feedback – no ability to “hear” sounds that happened in the past
Can be annoying, unsuitable for public use

## Slide 11: Types of audio interaction?

## Slide 12: Types of audio interaction
Audio as part of existing content (e.g. video)
Non-speech audio output
  Sound effects / feedback
  Notification sounds
    Events
    System status
Speech output / text-to-speech
Input (mostly speech, some non-speech)

## Slide 13: Audio perception

## Slide 14: Audio perception
Key components: frequency, loudness, position, timbre, duration
  Also patterns of audio (rhythm, melody)
Perceivability — often it’s easier to detect relative differences (this tone became louder or higher) than identifying sounds out of context
  Strong individual differences in audio perception ability
Adapted from Brewster, Non-speech audio output, HCI Handbook, 2002.

## Slide 15: Components
Frequency — 20 Hz to 20 KHz, varies by individual, age, etc.)
  Most people can sense changes in frequency; 1% can accurately identify
Loudness — can compare loudness, can be difficult to measure absolute loudness
  Most people can detect ~3 gradations of absolute loudness
Position — can sometimes dbetween 1 deg

## Slide 16: More components
Position — detect differences in position relative to the listener’s head
  Varies from 1 degree to about 40 degrees based on location
  More difficult to detect movement at one side
Timbre — the “quality” of sound (e.g. piano vs. guitar)
  Typically easy to recognize
  But no natural ordering (does guitar come before or after piano?)

## Slide 17: Quirks of audio perception
Ability to discriminate sounds varies by their intensity
  Easier to detect small changes in low frequency sounds or volume (Weber’s law)
Interactions between characteristics
  For sounds < 2k Hz, increasing loudness increases perceived pitch
  For sounds > 3k Hz, increasing loudness decreases perceived pitch

## Slide 18: Quirks of audio perception
Ability to discriminate sounds varies by their intensity
  Easier to detect small changes in low frequency sounds or volume (Weber’s law)
Interactions between characteristics
  For sounds < 2k Hz, increasing loudness increases perceived pitch
  For sounds > 3k Hz, increasing loudness decreases perceived pitch
Audio illusions (more on this later…)

## Slide 19: Weber’s law (1834)
Ratio of the just noticeable difference (JND ∆I) to initial stimulus I is a constant k across magnitudes of that stimulus
i.e., the JND is a constant proportion of the original stimulus value
Notes: True for all stimuli, not just sound

## Slide 20: Weber’s law demo
Brad Way on YouTube
Notes: True for all stimuli, not just sound

## Slide 21: Context effects
Audio perception may be impacted by context
  Background sounds
  Position of sound relative to user
May be further impacted by social factors
  People may not want to use speech input in public
  May lower volume / mute devices

## Slide 22: Connecting back to Norman/Nielsen
What is audio good for?
  Feedback
  Indicating system status
  Representing mappings (sometimes)

## Slide 23: Designing sound and representing data

## Slide 24: Goals of sonification
Represent some data using sound
  Starting with raw data, or an existing visual representation
As with visual processing, we want to represent many different types of information
  Relationships between multiple objects
  Changes over time
  …

## Slide 25: Why we should care
Often we talk about sonification as an accessibility feature
  Making complex data accessible non-visually
Key question here about mappings and perceived characteristics of audio
Also relevant to designing other sounds
  Is this a success or failure sound?

## Slide 26: Representing things visually or sonically
Our ability to process information visually is very different than audio perception
This makes it difficult to translate from one to the other
In many cases, the best solution is to present information in multiple modes (“multimodally”)

## Slide 27: Visual information (compared to audio)
Visual information is…
+ High bandwidth (1334 x 750 x 30 fps)
+ Easy to overlay and show multiple items
+ Easy to make information self-describing (with text)
+ Can rely on visual conventions (color, icons)
+ Easier to structure information
+ Can often browse or scan through information, and return back later
+ Can represent 2D or 3D
– Requires active attention
– Not always accessible

## Slide 28: Audio mappings
So, does audio have mappings? Are they natural mappings?

## Slide 29: Do audio mappings exist?
What is natural, what is cultural convention, what is learned?

## Slide 30: Audio mappings
Some sounds are very recognizable (with training):
Can represent calmness or alertness:
Can represent affect:
Can represent changes in quantity:
Notes: To be clear, sometimes it’s hard to disambiguate why we feel this way.

## Slide 31: Sound mappings
Pitch, tempo → map to increasing and decreasing value
Stereo position → can map to actual position... maybe to value (but not necessarily)
Most everything else needs to be learned

## Slide 32: Mappings can be weird
Walker and Mauney, Universal Design of Auditory Graphs… TACCESS 2(3), 2010

## Slide 33: Mappings can be weird
Walker and Mauney, Universal Design of Auditory Graphs… TACCESS 2(3), 2010

## Slide 34: But what about 3D audio?
Can we just put everything in 3D?
Some specialized 3D audio systems use multiple audio sources (e.g. Ossic)
Simulated 3D audio uses stereo speakers and a model of the human head (head related transfer function or HRTF)
  Works well when combined with visuals, or made responsive to head movements)
  Not as effective on its own
  Users may not always want to wear headphones

## Slide 35: Audio aesthetics
Can audio make something sound “better”?
Sounds can indicate high quality components, materials, attention to detail…
Video: BMW designers on designing the sounds of their cars

## Slide 36: Audio illusions
Shepard Tones — audio appears to constantly rise (or fall) in pitch
Notes: Human perception is interesting and if we understand it, we can do interesting things

## Slide 37: Speech (briefly*) * more on this in Shaun’s Spring CSCI 7000 course

## Slide 38: Speech input
Today it is easy to use speaker-independent, untrained speech input
  This is a big deal and relatively recent
Array microphones (e.g. Amazon Echo) enable speech input at a distance
Designing effective speech interfaces is an open challenge

## Slide 39: Challenges to speech input
When is system listening?
How do users know what to say?
  Telling users they can use “natural language” is a big risk, if the system gets it wrong
Natural language commands can take many forms
  Both phrasing and structure of command
  “Send a message”, “Send a message to Kevin”, “Message Kevin”, ”Tell Kevin that I’m going to be late”
Handling errors can be confusing — users may get louder, enunciate more (which might not help)
Best solution may vary based on context (mobile vs. home vs. shared office vs. private office)

## Slide 40: Speech output
Becoming more common in mainstream technology
  More natural voices
This is a moving target as users become more accustomed to interacting with voice
Speech rates vary widely
  Human speech ~150 words per minute; expert screen reader users up to 500 wpm
Notes: Screen reader users often prefer less natural voices; artificial voices may be more intelligible at high speed

## Slide 41: Screen readers are fast
Rhea Guntalilib, How Blind People Use Computers
Notes: Screen reader users often prefer less natural voices; artificial voices may be more intelligible at high speed

## Slide 42: Interesting applications of audio

## Slide 43
http://sonify.psych.gatech.edu/research/aquarium/
http://sonify.psych.gatech.edu/research/aquarium/

## Slide 44: Earcons and spearcons
Examples from ICAD
Earcons
  Open
  Paint
Spearcons
  Elephant
  Braxton Philbrick
Tactons → haptic signals

## Slide 45: Nomadic Radio

## Slide 46: The VOICE
Use computer vision to sonify the environment
Map various feature detectors to sound
Requires extensive training (and may not actually be useful…)

## Slide 47: Hearables and audio AR
Wireless headphones that can be worn all day
“Pass through” augmented audio
  Here - selective noise cancellation
  Pixel Buds - real-time translation
Issues around battery life, comfort, social acceptability?
Notes: Image from The Verge

## Slide 48: Voice input

## Slide 49: Vocal Joystick and VoiceDraw
How to use speech input if you cannot speak (or cannot speak clearly)?
Use nonspeech vocal sounds as input

## Slide 50: VoiceDraw video

## Slide 51: Dual-Purpose Speech

## Slide 52: Sonifications
SAS graphics accelerator
Tangible interactive sonification
sound/tracks
Altering walking sounds
Real time finance sonification
Listen to Wikipedia
Eclipse Soundscapes
Sonification Sandbox

## Slide 53: How to design a sonification
What is it that you want to communicate about the data? (top 2-4 variables)
  What are the variables? Do we know their range, distribution?
Interactive, single sound, or sequence of sounds?
Order data in a logical way (if possible)
Map data (and inputs, if interactive) to outputs

## Slide 54: Inputs and outputs
Inputs
Data itself
Touch or keyboard input
Outputs
Timbre / instrument
Pitch
Volume
Stereo position
Other audio effects (vibrato, high/low pass filter, etc)

## Slide 55: Assignment
We are going to design sonification mappings
Time in class to experiment with ideas, tools